## Slide 1
ÉPOQUE: Environmental POrtfolio for Quality in University Education
COURSE III
Entrepreneurship – Intelligent energy
MODULE 1
Intelligent energy

## Slide 2
TOPIC 3
The smart grid concept
2 # 29

## Slide 3: EXISTING ELECTRICITY/POWER GRID
It is a network delivering electricity from suppliers to consumers
  Electricity providers running power generating stations (1)
  Sub-stations transforming voltage upwards and downwards (2, 4)
  Transmission lines to carry high voltage electrical power (3)
  Distribution lines to connect consumers with the electricity grid (5)
3 # 29

## Slide 4: CURRENT GRID’S LIMITATION
Ageing infrastructure without recent evolvements – slow response times due to mechanical parts
Energy efficiency, environmental issues and consumers’ needs are not central in its design
Very limited visibility and flexibility
Lack of situation-awareness and automated analyses of operational conditions
One-way communication between supply and demand
Inefficient power supply security
Inability to store generated energy
4 # 29

## Slide 5: DRIVERS FOR AN “INTELLIGENT” APPROACH
Electricity demands will rise heavily (heat pumps, electric vehicles) and current grid has almost reached its limit
Flexible architectures to integrate new energy sources and technologies for energy storage and balancing demand with supply
Renewable energy sources (especially wind) are fluctuating and require enhanced management and control capabilities of the energy system
Need to provide energy storage capabilities, improve the security of supply and to lower carbon emissions
5 # 29

## Slide 6: SMART GRID
“A smart grid is an electricity network that can intelligently integrate the actions of all users connected to it - generators, consumers and those that do both – in order to efficiently deliver sustainable, economic and secure electricity supplies.”
6 # 29

## Slide 7: DEFINING SMART GRID
A smart grid is an electricity network that uses digital and other advanced technologies to monitor and manage the transport of electricity from all generation sources to meet the varying electricity demands of end-users.
Smart grids co-ordinate the needs and capabilities of all generators, grid operators, end-users and electricity market stakeholders to operate all parts of the system as efficiently as possible, minimizing costs and environmental impacts while maximizing system reliability, resilience and stability.
7 # 29

## Slide 8: SMART GRID ARCHITECTURE
8 # 29

## Slide 9: INTELLIGENT VS CONVENTIONAL GRID
Existing grid | Intelligent grid
Electromechanical | Digital
One-way communication | Two-way communication
Centralised generation | Distributed generation
Hierarchical | Network
Few sensors | Sensors throughout
Blind | Self-monitoring
Manual restoration | Self-healing
Failures and black-outs | Adaptive and islanding
Manual check/test | Remote check/test
Limited control | Pervasive control
Few customer choices | Many customer choices
9 # 29

## Slide 10: SMART GRID’S OBJECTIVES
Overcome the limits on the development of distributed generation and storage
Increase efficiency of the electricity grid and reduce electricity grid wastage
Ensure interoperability, robustness and security of supply even under the instance of emergency issues including self-healing abilities
Provide accessibility for all the users to a liberalized market
Reduce the impact of environmental consequences of electricity production and delivery
10 # 29

## Slide 11: SMART GRID CONCEPTUAL MODEL
11 # 29

## Slide 12: SMART GRID DOMAINS & ACTORS
Domain | Actors in the Domain
Customers | The end users of electricity. May also store, and manage the use of energy. Traditionally, three customer types are discussed, each with its own domain: residential, commercial, and industrial.
Markets | The operators and participants in electricity markets.
Service Providers | The organizations providing services to electrical customers and utilities.
Operations | The managers of the movement of electricity.
Bulk Generation | The generators of electricity in bulk quantities. May also store energy for later distribution.
Transmission | The carriers of bulk electricity over long distances. May also store and generate electricity.
Distribution | The distributors of electricity to and from customers. May also store and generate electricity.
12 # 29

## Slide 13: SMART GRID’S KEY SUCCESS FACTORS
Reliable – provides power dependably, warns for and withstands failures, takes timely corrective actions
Secure – resists to physical and cyber attacks and it is less vulnerable to natural disasters
Economic – fair prices and adequate supply
Efficient – cost control, reduced transmission and distribution losses, more efficient power production
Environmentally friendly – reduces environmental impacts in every part of the energy system
Safe – does no harm to the public or to grid workers
13 # 29

## Slide 14: INTELLIGENT ENERGY CHAIN
14 # 29

## Slide 15: SMART GRID’S DEFINING TRAITS
Operates resiliently to disturbances, physical attacks and natural disasters
Enabling active consumer participation in demand response
Providing power quality for the 21st century needs
Accommodating all generation and storage options
Enabling new products, services, and markets
Optimizing assets and operating efficiently
15 # 29

## Slide 16: SELF-HEALING GRID
A self-healing grid is expected to respond to threats, material failures, and other destabilizing influences by preventing or containing the spread of disturbances through:
  Constantly monitoring its components and tunes itself to run at an optimum state
  Probabilistic risk assessments based on real-time measurements to identify potential components to fail
  Real-time contingency analyses to determine overall grid health
  Communications with local and remote devices to identify grid conditions and take control actions
16 # 29

## Slide 17: ISOLATING PROBLEMS
17 # 29

## Slide 18: GRID RESILIENCY
Reduced system vulnerability to physical or cyber attack
Identification of threats and vulnerabilities – Enhanced critical threat information with closer ties between system operators and government
Protecting the network – Implementation of security technologies, such as authorization, authentication, encryption and intrusion detection
Inclusion of security risk in system planning – Anticipating the effects of a coordinated terrorist attack in system-wide planning
18 # 29

## Slide 19: ACTIVE CONSUMER PARTICIPATION
Consumers choose when, where, and how much electricity they consume, generate, and store
The new term “energy prosumer” is an energy market participant who both produces and consumes energy.
System elements that inform the customer about the cost and value of their consumption in real time
Improved control over home energy bills
Incorporate their Plug-in Hybrid Electric Vehicles (PHEV) and Electric Vehicles (EV) into the home, office, etc.
19 # 29

## Slide 20: HIGH QUALITY POWER
Technologies and devices on the distribution grid to manage the delivered voltage and power
Voltage personalizes optimization for each consumer—supply based on actual consumer voltages
Limiting/buffering voltage sags and surges on the grid
Modern switching and advanced maintenance that help service providers prevent momentary power fluctuations from reaching users of digital devices
Voltage imbalances reported by networked meters to service providers for immediate repair
20 # 29

## Slide 21: HIGH QUALITY POWER
21 # 29

## Slide 22: MULTIPLE GENERATION & STORAGE OPTIONS
Enables "plug-and-play" interconnection to multiple and Distributed Energy Resources (DER)
Improved interconnection standards to enable a wide variety of generation and storage options
Easier and more profitable for commercial users to install their own generation and storage facilities.
Large environmentally-friendly central plants will be readily integrated into the transmission system and fossil fuel usage will be reduced
Decentralized model that includes a balance of large, centralized generating plants as well as DER
22 # 29

## Slide 23: DECENTRALIZED POWER GRID
23 # 29

## Slide 24: ENABLES MARKETS
Modern grid will enable more market participation through:
  increased generation paths
  more efficient aggregated demand response initiatives
  placement of energy storage and resources within a more reliable distribution system
Brokers, integrators, aggregators and enabled consumers will interact in real time with the electricity market
By reducing congestion, the modern grid expands markets; it brings together more buyers and sellers
New electricity markets will emerge by the introduction of new commercial goods and services (e.g. clean energy)
24 # 29

## Slide 25: OVERVIEW OF THE MARKETS DOMAIN
25 # 29

## Slide 26: OPTIMIZING ASSENTS AND OPERATING EFFICIENTLY
Assets will be managed to deliver only what is needed and only when it is needed
Integration of near real-time data with advanced algorithms to improve decision-making and optimize both the capacity and the quality of electrical services
With near real-time data, condition-based maintenance will dramatically improve equipment failure rates and reduce their maintenance costs
Advanced Outages Management Systems (OMS) will significantly reduce the time to detect, locate, and diagnose outages
26 # 29

## Slide 27: SMART GRID BENEFITS
Defining trait | Benefit
Self-healing | Enhances cost savings, reliability and the profitable marketing of surplus power.
Active consumer participation | Consumers use more wisely, helping utilities produce more efficiently resulting in a wide range of environmental benefits
Resists attack | The grid deters or withstands physical or cyber attack
High quality power | Avoids productivity losses of downtime, especially in digital device environments
Multiple generation & storage options | Diverse resources with “plug-and-play” connections multiply the options for electrical generation and storage including new opportunities for more efficient, cleaner power production
Enables markets | The grid’s open-access market reveals waste and inefficiency and helps drive them out of the system while offering new consumer choices such as green power products.
Optimizes assets & operates efficiently | Desired functionality at minimum cost guides operations and the use of assets
27 # 29

## Slide 28: BIBLIOGRAPHY
European SmartGrids Technology Platform (2006). Vision and Strategy for Europe’s Electricity Networks of the Future
Faranghi, H. (2010). The Path of the Smart Grid, IEEE power and energy magazine, 8(1), 18-28
National Institute of Standards and Technology. NIST Framework and Roadmap for Smart Grid Interoperability Standards Release 1.0 (Draft), 2009
National Energy Technology Laboratory (2010), Understanding the Benefits of Smart Grids, Pittsburgh
U.S. Department of Energy (2010). The Smart Grid: An Introduction, Washington, DC.
28 # 29

## Slide 29: IMAGE SOURCES
http://www.nature.com/news/2008/080730/images/454570a-6.jpg
http://www.whatissmartgrid.org/smart-grid-101/fact-sheets/smart-grid-and-power-quality
http://indiasmartgrid.org/en/technology/Pages/Distributed-Generation.aspx
29 # 29