## Slide 1
ÉPOQUE: Environmental POrtfolio for Quality in University Education
COURSE III
Entrepreneurship – Intelligent energy
MODULE 1
Intelligent energy

## Slide 2
TOPIC 3
Smart grid components and technologies
2 # 25

## Slide 3: SMART GRID COMPONENTS
Intelligent appliances
Smart power meters
Smart substations
Smart generation
Smart distribution
3 # 25

## Slide 4: INTELLIGENT APPLIANCES
Intelligent appliances are providing residential power consumers with insight into their energy consumption, facilitating energy-efficient and eco-friendly behavior
Enable monitor of their usage and support remote management
Capable of deciding when to consume power based on pre-set customer preferences
Best candidates are the appliances consuming a lot of power and can be used with discretion, such as the HVAC (Heating Ventilation A/C) system, washers and dryers
Consumers can save up to 25% on their energy usage
4 # 25

## Slide 5: INTELLIGENT APPLIANCES - EXAMPLES
5 # 25

## Slide 6: SMART POWER METERS
Digital devices for measuring various features relative with electricity consumption
Provide data on electricity price and consumption, CO2 emissions and show comparisons of energy usage on a given time frame basis
Support two-way flow of information between them and electricity provider
Enable demand response – that is actions taken to reduce the energy demand by end users
6 # 25

## Slide 7: SMART GENERATION
Optimize the production of electricity utilizing different energy sources efficiently, flexible, fast and with cost-effectively
Balance multiple energy sources to meet network requirements and consumption needs – balancing supply and demand
Maintain voltage, frequency and power factor standards based on feedback from multiple points in the grid
Each generator runs independently of the others (all run in parallel) and runs only when needed (based on load)
7 # 25

## Slide 8: SMART DISTRIBUTION
Supports distributed energy resource deployment
Enables self-healing, self-balancing and self-optimizing and autonomous restoration
Utilizes the bi-directional flow of information to optimize distribution grid operations
Enhances security of supply and power quality
Automated monitoring and analysis tools capable of detecting or even predicting cable and failures based on real-time data about weather, outage history
8 # 25

## Slide 9: SMART SUBSTATIONS
Achieve the intelligent management of substation equipments by advanced data analysis processing methods based on advanced sensor technologies
Support a series of sophisticated functions such as intelligent alarm and analysis, substation load transfer, device status visualization, battery monitoring, etc.
9 # 25

## Slide 10: SMART GRID TECHNOLOGICAL AREAS
Wide area monitoring and control
Renewable and distributed generation integration
ICT integration
Transmission enhancement applications
Distribution grid management
Advanced metering infrastructure (AMI)
EV charging infrastructure
Customer-side systems (CS)
10 # 25

## Slide 11: TECHNOLOGY SPAN IN THE SMART GRID
11 # 25

## Slide 12: WIDE AREA MONITORING AND CONTROL
Real-time monitoring and display of power system components and performance
Advanced system operation tools to avoid blackouts and facilitate the integration of renewable energy resources
Monitoring and control technologies along with advanced system analytics:
  Supervisory control and data acquisition (SCADA)
  Wide-area situational awareness
  Wide-area monitoring systems
  Wide-area adaptive protection, control and automation
12 # 25

## Slide 13: MONITORING THE GRID
13 # 25

## Slide 14: RENEWABLE AND DISTRIBUTED GENERATION INTEGRATION
Challenges for their dispatchability and controllability and for operation of the electricity system
Energy storage systems can decouple the production and delivery of energy
Automation of control of generation and demand to ensure balancing of supply and demand
Power conditioning equipment for bulk power and grid support
Communication and control hardware for generation and enabling storage technology
14 # 25

## Slide 15: ICT INTEGRATION
Create a dynamic, high-speed interactive infrastructure for real-time information and power exchange
System control software and enterprise resource planning (ERP) software to support the two-way exchange of information between stakeholders
Wireless technologies :
  IEEE.802.11 (WiFi)
  IEEE.802.16 (WiMax)
  GSM/GPRS
Wired technologies:
  Fiber optics
  xDSL
  Power Line Communication
15 # 25

## Slide 16: COMMUNICATION TECHNOLOGIES
16 # 25

## Slide 17: TRANSMISSION ENHANCEMENT APPLICATIONS
Flexible AC transmission systems (FACTS) are used to enhance the controllability of transmission networks and maximize power transfer capability
High voltage DC (HVDC) technologies are used to connect offshore wind and solar farms to large power areas
Dynamic line rating (DLR), can optimize utilization of existing transmission assets, without causing overloads
High-temperature superconductors (HTS) can reduce transmission losses and enable economical fault-current limiting with higher performance
17 # 25

## Slide 18: DISTRIBUTION GRID MANAGEMENT
Distribution and sub-station sensing and automation can:
  reduce outage and repair time
  maintain voltage level
  improve asset management
Sensor technologies enable condition- and performance-based maintenance of network components
Geographic Information System (GIS), Distribution Management System (DMS), Outage Management System (OMS), Workforce Management System (WMS)
18 # 25

## Slide 19: DISTRIBUTION GRID MANAGEMENT SYSTEM
19 # 25

## Slide 20: ADVANCED METERING INFRASTRUCTURE
Remote consumer price signals, which can provide time-of-use pricing information
Collect, store and report customer energy consumption data for any required time intervals or near real time
Improved energy diagnostics from more detailed load profiles
Ability to identify location and extent of outages remotely via a metering function that sends a signal when the meter goes out and when power is restored
Losses and theft detection
20 # 25

## Slide 21: EV CHARGING INFRASTRUCTURE
Handles billing, scheduling and other intelligent features for smart charging (grid-to-vehicle)
large charging installation will provide power system ancillary services, such as capacity reserve, peak load shaving and vehicle-to-grid regulation
21 # 25

## Slide 22: CUSTOMER-SIDE SYSTEMS
Help manage electricity consumption at the industrial, service and residential levels
Include energy management systems, energy storage devices, smart appliances and distributed generation
Energy efficiency gains and peak demand reduction can be accelerated with in-home displays/energy dashboards, smart appliances and local storage
Automated, price-responsive appliances and thermostats connected to an energy management system or controlled from the utility or system operator
22 # 25

## Slide 23: SMART GRID - SUMMARY
Evolves traditional power system through monitoring and control, self-healing, automation, security etc.
Provides consumers with information related to their energy usage (e.g. cost, alternative options etc.)
Integrates renewable energy sources
Adds energy storage abilities into the system
These lead to an energy system that is more reliable, sustainable and resilient.
23 # 25

## Slide 24: BIBLIOGRAPHY
National Energy Technology Laboratory (2007). A systems view of the modern grid, white paper
Wakefield, M., Nowaczyk, J., and Handley, J. (2014). From Research to Action: Communication Research and Actions to Enable the Future Electric Power System. Electric Energy T&D, 97, 772
24 # 25

## Slide 25: IMAGE SOURCES
http://www.nytimes.com/2012/01/22/us/comeds-smart-grid-begins-with-a-promise-for-the-future.html
http://www.thinkinggrids.com/smart-grid-news/the-future-of-distribution-management-systems
http://www.autoevolution.com/news/us-homebuilder-offers-ev-charging-infrastructure-preparation-17831.html
25 # 25